## Slide 1: CFD Lab 1 Simulation of Turbulent Pipe Flow Created by Seong Mo Yeon, Timur Dogan Edited by Michael Conger, Dong-Hwan Kim
Notes: Introduce yourself
Introduce Lab – Simulation of Laminar Pipe Flow in smooth pipe

## Slide 2: Outline
Overview of Pipe Flow
CFD Process
Geometry
Mesh
Physics
Results

## Slide 3: Overview of Pipe Flow
Simulation of turbulent pipe flow will be conducted for this lab
Axial velocity profile, centerline velocity, centerline pressure, and wall shear stress will be analyzed
Computational fluid dynamics (CFD) results for friction factor and velocity profile and centerline pressure will be compared to experimental fluid dynamics (EFD)
This lab will cover concept of laminar vs. turbulent flow and developing length for pipe flows
Notes: Questions:
What is the velocity at the wall?
Talking Points:
Simulating laminar pipe flow
Comparing CFD results to AFD solutions
Look at the developing profile
  Uniform inlet to quadratic
  Linear pressure drop in fully developed flow
  Developing length

## Slide 4: Overview of Pipe Flow
Flow in pipe with Reynolds number (Re)
  where U is an inflow velocity, D is a diameter of pipe, is a kinematic viscosity
  Laminar : Re < 2300
  Turbulent : Re > 2300
Turbulent flow features
  Irregularity
  Diffusivity
  Dissipation
  Energy cascade
Analysis of turbulent flow
  Mean value in time vs. space
  Turbulent model
    Reynolds stress model (in RANS)
    k-epsilon model
Flow visualization of transition from laminar to turbulent flow
Turbulent mixing flow in pipe
Notes: Talking Points:
Laminar flow is viscous dominated
  Low Re #
Turbulent flow is inertial dominated
  High Re #

## Slide 5: CFD Process
The overall procedure for simulation of pipe flow is shown on chart below
Although we will be making the mesh before we define the physics you have to know the physics to design appropriate mesh.
Geometry
Physics
Mesh
Solution
Results
Pipe (ANSYS Design Modeler)
Structure (ANSYS Mesh)
Non-uniform (ANSYS Mesh)
General (ANSYS Fluent - Setup)
Model (ANSYS Fluent - Setup)
Boundary Conditions (ANSYS Fluent -Setup)
Reference Values (ANSYS Fluent - Setup)
Turbulent
Solution Methods (ANSYS Fluent - Solution)
Monitors (ANSYS Fluent - Solution)
Solution Initialization (ANSYS Fluent -Solution)
Plots (ANSYS Fluent- Results)
Graphics and Animations (ANSYS Fluent- Results)
Notes: Talking Points:
Physics must be known to properly construct mesh/grid
  Example: must know if flow is turbulent to determine grid refinement for B.L.
    Need many grid points to resolve large velocity grads noticed in turbulent B.L.
In ANSYS mesh comes before physics

## Slide 6: ANSYS Design Modeler (Geometry)
Parameter | Value
Radius of pipe, R | 0.02619 m
Diameter of pipe, D | 0.05238 m
Length of pipe, L | 6.096 m
L
R
D
Symmetric property of the flow is used to create 2D representation of the 3D pipe flow
Inlet
Outlet
Wall
Center
Flow
=location of the EFD pressure tab #4,
and will be treated as an outlet in CFD
Notes: Talking Points:
In CFD it is best to simplify problem for efficiency
Pipe can be simplified into 2D rectangle axisymmetric about centerline

## Slide 7
Previously, in Pre-lab1, uniform grid distribution was used for laminar flow
Velocity profile of turbulent flow need more resolution near the wall
because of its larger velocity gradient (𝑑𝑢/𝑑𝑟) near the wall than in laminar flow
Non-uniform mesh is better for the turbulent flow
ANSYS Mesh
Laminar
Turbulent
Notes: Talking Points:
CFD is discretizing the fluid flow and solving N.S. eqns numerically at each grid point
Discretize geometry by splitting sides
Can get information at any discretized point

## Slide 8
Turbulent flow
Air properties (Need to be extracted from the EFD)
Boundary Conditions (BC) (Need to be extracted from the EFD)
  No-slip: velocities and pressure gradient is zero ( )
  Symmetric: radial velocity and gradients of axial velocity and pressure are zero (, , )
  Inlet velocity: uniform constant velocity ()
  Outlet: (gauge) pressure is imposed to the boundary (, , EFD tab 4 pressure)
Inlet –
Velocity inlet BC
Outlet –
Pressure outlet BC
Wall – No slip BC
Center – Axisymmetric BC
Flow
ANSYS Fluent – Physics
Zero slop at center or
r
x
“CFD Input” tab in “EFD Lab 2 Data Reduction Sheet”
Notes: Talking Points:
No slip wall
Symmetric about axis for axial velocity and pressure
Uniform inlet velocity
Outlet pressure

## Slide 9
Validation of the wall friction factor
ANSYS Fluent – Results
FactorCFD | FactorEFD | %Error
0.01745 | 0.01801 | 3.07
Validation of the velocity profile at the developed region and the pressure distribution
Notes: Questions:
Can anyone explain what fully developed flow is?
Why is friction coefficient constant in fully developed
Talking Points:
Explain developing length
Linear pressure drop in fully developed

## Slide 10
ANSYS Fluent – Results
Developing
region
Developed region
Developing
region
Developed region
Laminar
Turbulent
Notes: Questions:
Can anyone explain what fully developed flow is?
Why is friction coefficient constant in fully developed
Talking Points:
Explain developing length
Linear pressure drop in fully developed

## Slide 11: Questions?
Deadline for the CFD Lab 1 report is two weeks after from your CFD lab 1 (Today)
Please download the “CFD Lab1 Report Template.doc” under the “CFD Lab 1” section in the website, and fill out both Pre-lab1 and Lab1 answers (there’s no separate report for the Pre-lab 1)
Pre-lab 1 questions will be graded separately, so it doesn’t need to be attached to the report
Use the Lab drop-box when turning in your lab reports
Come to the office hours for any help