## Slide 1: CFD Pre-Lab 2 Simulation of Turbulent Flow Around an Airfoil Created by Seong Mo Yeon, Timur Dogan Edited by Dong-Hwan Kim
Notes: Introduce yourself
Introduce Lab – Simulation of Laminar Pipe Flow in smooth pipe

## Slide 2: Outline
Overview of Flow Around Airfoil
CFD Process
Geometry
Mesh
Physics
Results

## Slide 3
Simulation of the flow around the airfoil will be conducted for this lab
Computational fluid dynamics (CFD) results for drag and lift coefficients, coefficient of pressure around the airfoil will be compared to experimental fluid dynamics (EFD)
This lab will cover concept of boundary layer and flow separation
Overview of Flow Around Airfoil
Flow visualization around airfoil
(starts at 5:34)
Notes: Questions:
What is the velocity at the wall?
Talking Points:
Simulating laminar pipe flow
Comparing CFD results to AFD solutions
Look at the developing profile
  Uniform inlet to quadratic
  Linear pressure drop in fully developed flow
  Developing length

## Slide 4
Boundary Layer
  Defined by Ludwig Prandtl
  Generated by viscosity near wall
  Cause of lift and drag forces
  Inviscid vs. viscous flow
  Flow separation
  Note: Refer to Chapter 9 of your book for more details
Overview of Flow Around Airfoil
Flow visualization of boundary layer
(Start at 3:21)
Notes: Talking Points:
Laminar flow is viscous dominated
  Low Re #
Turbulent flow is inertial dominated
  High Re #

## Slide 5: CFD Process
The overall procedure for simulation of flow around airfoil is shown on chart below
Although we will be making the mesh before we define the physics you have to know the physics to design appropriate mesh.
Geometry
Physics
Mesh
Solution
Results
Airfoil (ANSYS Design Modeler)
Structured (ANSYS Mesh)
Non-uniform (ANSYS Mesh)
General (ANSYS Fluent - Setup)
Model (ANSYS Fluent - Setup)
Boundary Conditions (ANSYS Fluent -Setup)
Reference Values (ANSYS Fluent - Setup)
Turbulent
Solution Methods (ANSYS Fluent - Solution)
Monitors (ANSYS Fluent - Solution)
Solution Initialization (ANSYS Fluent -Solution)
Plots (ANSYS Fluent- Results)
Graphics and Animations (ANSYS Fluent- Results)
C-Domain (ANSYS Design Modeler)
O-Domain (ANSYS Design Modeler)
Solution Initialization
(ANSYS Fluent - Solution)
Solution Controls (ANSYS Fluent - Solution)
Run Calculation
(ANSYS Fluent - Solution)
Notes: Talking Points:
Physics must be known to properly construct mesh/grid
  Example: must know if flow is turbulent to determine grid refinement for B.L.
    Need many grid points to resolve large velocity grads noticed in turbulent B.L.
In ANSYS mesh comes before physics

## Slide 6: ANSYS Design Modeler (Geometry)
Import Clark-Y airfoil geometry
Split O-type domain into four pieces
Parameter | Value
Chord length, c | 0.3048 m
Diameter of domain, Rc | 12.0 m
Angle of attack, α | 0, 16
Notes: Talking Points:
In CFD it is best to simplify problem for efficiency
Pipe can be simplified into 2D rectangle axisymmetric about centerline

## Slide 7
Fine mesh at the boundary layer region to resolve large velocity gradients
ANSYS Mesh
Notes: Talking Points:
CFD is discretizing the fluid flow and solving N.S. eqns numerically at each grid point
Discretize geometry by splitting sides
Can get information at any discretized point

## Slide 8
Turbulent flow
Viscous & Inviscid models
Air properties (Need to be extracted from the EFD)
Boundary Conditions (BC) (Need to be extracted from the EFD)
  No-slip (airfoil surface): velocities and pressure gradient are zero ( )
  Inlet velocity: uniform constant velocity ()
  Outlet: (gauge) pressure is imposed to the boundary (, , 0)
(where ‘n’ is the normal vector)
ANSYS Fluent – Physics
Inlet – Velocity inlet BC
Outlet – Pressure outlet BC
Wall – No slip BC
Notes: Talking Points:
No slip wall
Symmetric about axis for axial velocity and pressure
Uniform inlet velocity
Outlet pressure

## Slide 9
If you have problems with solution convergence reduce Under-Relaxation Factors. This issue is more likely to occur for large angle of attack cases.
Also you may need to increase the number of iterations
ANSYS Fluent – Solution
Notes: Questions:
Can anyone explain what fully developed flow is?
Why is friction coefficient constant in fully developed
Talking Points:
Explain developing length
Linear pressure drop in fully developed

## Slide 10
ANSYS Fluent – Results
Chart: Coefficent of Pressure (Cp ) Distribution at 0 AOA
| 0 | 1.25 | 2.5 | 5 | 7.5 | 10 | 15 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 90 | 80 | 70 | 60 | 50 | 40 | 30 | 20 | 15 | 10 | 7.5 | 5 | 2.5 | 1.25
Benchmark Data | 0.9879 | 0.87275 | 0.39262 | -0.11572 | -0.34115 | -0.45695 | -0.57559 | -0.66089 | -0.65602 | -0.6282 | -0.57327 | -0.49744 | -0.40916 | -0.30144 | -0.098318 | 0 | 0.046946 | -0.05244 | -0.07802 | -0.1303 | -0.11165 | -0.19364 | -0.23189 | -0.30989 | -0.33718 | -0.82684 | -0.93713 | -1.1188 | -1.3905 | -1.4784
Experimental-2013 | 0.7812 | 0.65696 | 0.28691 | -0.10742 | -0.29218 | -0.38378 | -0.46572 | -0.51752 | -0.51692 | -0.53112 | -0.49331 | -0.42692 | -0.3661 | -0.24688 | -0.087994 | 0 | 0.011353 | -0.050587 | -0.080591 | -0.10612 | -0.12649 | -0.15488 | -0.20482 | -0.2677 | -0.30445 | -0.6802 | -0.75038 | -0.90487 | -1.1274 | -1.1993
Experimental-2012 | 1.0012 | 0.93881 | 0.50718 | 0.047771 | -0.16439 | -0.28757 | -0.39747 | -0.46191 | -0.47683 | -0.44538 | -0.40957 | -0.33066 | -0.26565 | -0.21805 | 0.015108 | 0 | 0.12252 | 0.049338 | 0.01423 | -0.010254 | -0.040161 | -0.06886 | -0.13951 | -0.20041 | -0.24217 | -0.76022 | -0.81384 | -0.95607 | -1.2232 | -1.3722 | 0 | -0.0047966 | 1.04
experimental-2010 | 0.92146 | 0.87011 | 0.40445 | -0.10497 | -0.35682 | -0.49619 | -0.61401 | -0.69363 | -0.70588 | -0.67198 | -0.63468 | -0.55958 | -0.48509 | -0.36112 | -0.14643 | 0 | -0.026956 | -0.10538 | -0.14432 | -0.17979 | -0.20752 | -0.25024 | -0.31941 | -0.41675 | -0.47413 | -1.0559 | -1.1055 | -1.2929 | -1.545 | -1.7521 | 0 | 0.74534 | 1.0483
Chart: Coefficent of Pressure (Cp ) Distribution at 16 AOA
| 0 | 1.25 | 2.5 | 5 | 7.5 | 10 | 15 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 90 | 80 | 70 | 60 | 50 | 40 | 30 | 20 | 15 | 10 | 7.5 | 5 | 2.5 | 1.25
Benchmark Data | -0.78513 | -1.9842 | -2.2082 | -2.2091 | -2.0687 | -1.8836 | -1.6512 | -1.5204 | -1.0735 | -0.90726 | -0.75471 | -0.58686 | -0.41799 | -0.26672 | -0.11956 | 0.017092 | 0.022818 | 0.0084607 | 0.018203 | 0.035466 | 0.067258 | 0.10153 | 0.14075 | 0.20357 | 0.23647 | 0.27595 | 0.36022 | 0.4867 | 0.66215 | 0.92879
Experimental-2013 | -1.0407 | -2.079 | -2.2068 | -2.1553 | -1.9756 | -1.7956 | -1.5814 | -1.4491 | -0.99088 | -0.81033 | -0.67357 | -0.4864 | -0.33898 | -0.18745 | -0.056788 | 0 | 0.088208 | 0.10255 | 0.12082 | 0.13848 | 0.16837 | 0.197 | 0.23489 | 0.29129 | 0.3331 | 0.36934 | 0.45014 | 0.56751 | 0.70623 | 0.89801
Experimental-2010 | -0.74373 | -1.9366 | -2.1394 | -2.1264 | -1.967 | -1.819 | -1.5951 | -1.4675 | -1.0197 | -0.82208 | -0.66768 | -0.50561 | -0.34883 | -0.20626 | -0.062854 | 0 | 0.089281 | 0.079249 | 0.091889 | 0.10863 | 0.13627 | 0.16915 | 0.20257 | 0.26008 | 0.29433 | 0.31923 | 0.40004 | 0.53177 | 0.71142 | 0.948 | 0 | 0.016067 | 0.90048
experimental-2012 | -0.77838 | -1.8336 | -2.0123 | -2.0416 | -1.9243 | -1.7801 | -1.5669 | -1.44 | -1.0495 | -0.90082 | -0.77639 | -0.60222 | -0.42013 | -0.26677 | -0.13563 | 0 | 0.003821 | -0.010555 | 0.0023286 | 0.016461 | 0.039831 | 0.064767 | 0.094166 | 0.14247 | 0.17261 | 0.20438 | 0.26968 | 0.3764 | 0.53509 | 0.76929 | 0 | 0.67095 | 0.2274
Notes: Questions:
Can anyone explain what fully developed flow is?
Why is friction coefficient constant in fully developed
Talking Points:
Explain developing length
Linear pressure drop in fully developed

## Slide 11
ANSYS Fluent – Results
Pressure distribution around airfoil
Velocity vectors near wall and boundary layer development
Stream lines around airfoil
Notes: Questions:
Can anyone explain what fully developed flow is?
Why is friction coefficient constant in fully developed
Talking Points:
Explain developing length
Linear pressure drop in fully developed

## Slide 12: Questions?
Deadline for the CFD Lab 2 report is two weeks after from your CFD lab 2
(same as CFD Prelab1 & Lab1)
Pre-lab 2 questions will be graded separately, so it doesn’t need to be attached to the report
Bring EFD Lab3 Data Reduction Sheet for CFD Lab2, so that you can simulate AOA=16 degree case
Use the Lab drop-box when turning in your lab reports
Come to the office hours for any help